## Slide 1
<> ARC 500
Programming with Python and Generative AI · Scripting, Data Analysis, Visualization, Problem-Solving, and Optimization
WEEK 7 · MEETING A · SPATIAL DATA, SCALE, AND MAPS
Geometry needs a ruler before it means anything
Geometry vs. attributes, GeoDataFrame, CRS and EPSG codes, projected vs. geographic measurement, buffer, and spatial join
JunHo Chun, PhD · School of Architecture · Syracuse University · Fall 2026
Notes: Timing: 2 minutes.
Teaching notes: Open by asking: if I tell you two points are '0.000098 apart,' do you know how far apart they are? Today answers that question.

## Slide 2
PRINCIPLE
A map is only as trustworthy as its geometry and its CRS
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
02
Where something is, and what units that 'where' is measured in, are two separate facts you must both get right.
Geopandas will happily compute an area or a distance in the wrong coordinate reference system without stopping you. It is your job to notice.
Notes: Timing: 2 minutes.
Teaching notes: Foreshadow the two demonstrations coming later this deck: a distance measurement and an area measurement, both wrong in a geographic CRS, both fixed by reprojecting.

## Slide 3
LEARNING OUTCOMES
By the end, you should be able to…
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
03
1
Distinguish
Tell geometry (shape/location) apart from attributes (everything else) in one spatial table.
2
Choose
Pick point, line, or polygon geometry for a given architectural question.
3
Build
Read or build a GeoDataFrame and identify its CRS by EPSG code.
4
Reproject
Explain why area and length calculations require a projected CRS, then use buffer and spatial join correctly.
Notes: Timing: 2 minutes.
Teaching notes: Preview that all four skills feed directly into Meeting B's studio and into Project 1 Part IV's map option -- one of two evidence-extension choices (map or Week 6's animation), not an unconditional requirement.

## Slide 4
ROAD MAP
Today’s learning sequence
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
04
01
Geometry vs. attributes: two kinds of information, one table
02
Point, line, polygon: choosing the right geometry
03
GeoDataFrame, CRS, and EPSG codes
04
Why projection matters: buffer and spatial join
Notes: Timing: 2 minutes.
Teaching notes: Tell students the whole arc builds toward one static map they will produce themselves on Wednesday.

## Slide 5
NEW VOCABULARY
Geometry vs. attributes, defined
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
05
Geometry
The shape and location of a feature: a point, line, or polygon, stored in one special column (usually called geometry). Geometry answers 'where.'
Attributes
Every other column: room_type, zone, energy_kwh_m2_yr, and so on - ordinary pandas data describing 'what' about that location. A spatial table is just a regular table with one geometry column added.
Notes: Timing: 2 minutes.
Teaching notes: Point at a plain room schedule from Week 4-6: every column there is an attribute. Nothing in it says where a room actually is in space - that is exactly what today adds.
[Sources]
- https://geopandas.org/en/stable/getting_started/introduction.html
[/Sources]

## Slide 6
PYTHON SYNTAX
A plain pandas table has no geometry column yet
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
06
import pandas as pd
plain = pd.DataFrame({
'room_id': ['R101', 'R104'],
'room_type': ['Lobby', 'Studio'],
'x_m': [2.0, 2.0],
'y_m': [4.0, 22.0],
})
print(plain.dtypes)
OUTPUT
room_id str
room_type str
x_m float64
y_m float64
dtype: object
Attributes only, so far
x_m and y_m are just two float columns here - pandas has no idea they describe a location. Every dtype is a familiar Week 4 type: str or float64. Nothing here is 'spatial' yet.
Notes: Timing: 2 minutes.
Teaching notes: Ask: could you compute a distance between these two rows right now? Not really - x_m and y_m are still just numbers, not a geometry Python understands as a shape.
[Sources]
- https://pandas.pydata.org/docs/user_guide/index.html
[/Sources]

## Slide 7
PYTHON SYNTAX
points_from_xy turns coordinates into real geometry
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
07
import geopandas as gpd
geom = gpd.points_from_xy(plain['x_m'], plain['y_m'])
sites = gpd.GeoDataFrame(plain, geometry=geom, crs='EPSG:32618')
print(sites.dtypes)
OUTPUT
room_id str
room_type str
x_m float64
y_m float64
geometry geometry
dtype: object
One new column, one new dtype
gpd.points_from_xy(x, y) builds a Point geometry object per row from two plain columns. The result carries a geometry dtype - geopandas now understands these rows as locations, not just numbers. crs tells it which coordinate system those x_m/y_m numbers are already in.
Notes: Timing: 2 minutes.
Teaching notes: Point at the new geometry row in dtypes. This exact pattern - a plain table plus points_from_xy - is how you would turn any x/y attribute table into a spatial one.
[Sources]
- https://geopandas.org/en/stable/getting_started/introduction.html
[/Sources]

## Slide 8
VOCABULARY
GeoDataFrame, defined
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
08
TERM
GeoDataFrame
A pandas DataFrame with one extra column (geometry) holding shapely geometry objects, plus a coordinate reference system recording what those coordinates mean -- defined precisely a few slides from now. Everything you already know about DataFrames -- columns, dtypes, filtering, groupby, merge -- still works.
IN PRACTICE
gpd.GeoDataFrame(plain, geometry=..., crs=...)
Build one from a plain DataFrame plus a geometry column and a crs argument, exactly as the previous slide just did -- or load one directly with gpd.read_file(). GeoPandas adds exactly two things on top of pandas: a geometry column and a CRS.
COMMON CONFUSION
GeoPandas is not a new library to learn from scratch -- it is pandas plus a geometry column and a CRS. Today is about using both correctly.
Notes: Timing: 2 minutes.
Teaching notes: Reassure students: this is not 'yet another library,' it is pandas plus two additions. Reduces the perceived load of Week 7.
[Sources]
- https://geopandas.org/en/stable/getting_started/introduction.html
[/Sources]

## Slide 9
READ THE DATA
Point, line, and polygon answer different design questions
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
09
geometry type
stores
architectural example
Point
one x, y location
a site marker, a sensor, a room centroid
LineString
an ordered sequence of connected points
a circulation path, a property line, a utility run
Polygon
a closed boundary enclosing an area
a zone footprint, a building outline, a room outline
ARCHITECTURAL LENS
Choose the geometry type the design question actually needs - a distance question wants a line; an area question wants a polygon.
Notes: Timing: 2 minutes.
Teaching notes: Ask students to name one geometry type for their own Project 1 site before moving on - this previews Part IV's map option, one of two evidence-extension choices alongside Week 6's animation.
[Sources]
- https://geopandas.org/en/stable/getting_started/introduction.html
[/Sources]

## Slide 10
PYTHON SYNTAX
Point, line, and polygon are shapely objects with real properties
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
10
from shapely.geometry import Point, LineString, Polygon
site_marker = Point(2.0, 4.0)
egress_path = LineString([(2,4), (2,22), (18,22)])
zone_footprint = Polygon([(0,0), (24,0), (24,10), (0,10)])
print(site_marker.geom_type, site_marker)
print(egress_path.geom_type, 'length:', egress_path.length)
print(zone_footprint.geom_type, 'area:', zone_footprint.area)
OUTPUT
Point POINT (2 4)
LineString length: 34.0
Polygon area: 240.0
Coordinates already in meters here
These three literals use plain x, y numbers already understood to be meters (like Radley Hall's x_m/y_m columns), so .length and .area return sensible values right away - 34.0 m and 240.0 m2. The next slides show what happens when the coordinates are degrees of latitude/longitude instead.
Notes: Timing: 2 minutes.
Teaching notes: Confirm 240.0 m2 by hand: a 24 m x 10 m rectangle. Keep this number in mind - it reappears as Meeting B's known ground truth for the Radley Hall zone footprints.
[Sources]
- https://geopandas.org/en/stable/getting_started/introduction.html
[/Sources]

## Slide 11
VOCABULARY
CRS, defined
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
11
TERM
CRS
A Coordinate Reference System states what a pair of numbers (x, y or lon, lat) actually means: which surface, which units, and which origin. Without a CRS, coordinates are just numbers -- geopandas cannot tell you if they are meters, degrees, or feet.
IN PRACTICE
zones.crs
Printing a GeoDataFrame's .crs attribute reports the CRS geopandas currently has on record for it -- for example EPSG:4326 or EPSG:32618. Two GeoDataFrames must share a CRS before you can safely compare or join their geometries.
COMMON CONFUSION
A CRS is not a unit label typed into a column name -- it lives on the GeoDataFrame itself (gdf.crs), separate from any column, and travels with the geometry through most operations.
Notes: Timing: 2 minutes.
Teaching notes: Write both codes on the board - students will see exactly these two all studio long.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/projections.html
[/Sources]

## Slide 12
VOCABULARY
EPSG code, defined
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
12
TERM
EPSG code
A short numeric ID for one specific, standardized CRS, maintained by a public registry. Two codes recur constantly in this course: EPSG:4326 (geographic, degrees of latitude/longitude, the GPS standard) and EPSG:32618 (UTM zone 18N, meters, the correct projected choice for Syracuse, NY).
IN PRACTICE
crs='EPSG:32618'
Pass the EPSG code as a crs= argument when building a GeoDataFrame, or to set_crs()/to_crs() later -- always write it as the string 'EPSG:' followed by the number.
COMMON CONFUSION
EPSG:4326 is for storage and sharing - what GPS gives you. EPSG:32618 is for measuring - what you compute area, length, and distance with. The two are not interchangeable.
Notes: Timing: 2 minutes.
Teaching notes: Students will see exactly these two codes all studio long - 4326 for 'what GPS gives you,' 32618 for 'what you measure with.'
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/projections.html
[/Sources]

## Slide 13
PYTHON SYNTAX
gpd.read_file reports the CRS it found in the file
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
13
import geopandas as gpd
zones = gpd.read_file('zone_footprints.geojson')
print(zones)
print('CRS:', zones.crs)
OUTPUT
zone geometry
0 North POLYGON ((-76.1351 43.03936, -76.13481 43.0393...
1 South POLYGON ((-76.1351 43.0392, -76.13481 43.0392,...
CRS: EPSG:4326
Latitude/longitude, in degrees
This is the fictional Radley Hall zone-footprint file used in Meeting B - GeoJSON is a common text file format for storing geometry plus attributes together; gpd.read_file() reads it just like read_csv() reads a CSV. Its coordinates are longitude/latitude pairs - degrees, not meters - and geopandas correctly reports its CRS as EPSG:4326, the geographic default GPS coordinates arrive in.
Notes: Timing: 2 minutes.
Teaching notes: Point out the coordinate values themselves look like the Syracuse-area longitude/latitude students will recognize from the shared dataset README. Note North's row now has the higher-latitude coordinates - the file was corrected so the polygon plotted further north on the Northing axis is actually named North.
[Sources]
- https://geopandas.org/en/stable/getting_started/introduction.html
- https://geopandas.org/en/stable/docs/user_guide/projections.html
[/Sources]

## Slide 14
PYTHON SYNTAX
A geometry built without a CRS argument has none
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
14
from shapely.geometry import Point
import geopandas as gpd
gdf = gpd.GeoDataFrame({'room_id': ['R101']}, geometry=[Point(2.0, 4.0)])
print('crs before set_crs:', gdf.crs)
gdf = gdf.set_crs('EPSG:32618')
print('crs after set_crs:', gdf.crs)
OUTPUT
crs before set_crs: None
crs after set_crs: EPSG:32618
None is a real, common bug source
If you forget crs= when building a GeoDataFrame, gdf.crs is simply None - geopandas has no idea what the coordinates mean. set_crs() states what CRS the coordinates ALREADY are in; it does not move or change any numbers.
Notes: Timing: 2 minutes.
Teaching notes: Contrast set_crs (label an existing coordinate system) with to_crs, coming next (actually convert the numbers to a different system). Students confuse these two constantly - name the difference explicitly now.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/projections.html
[/Sources]

## Slide 15
VOCABULARY
Reprojection, defined
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
15
TERM
to_crs()
Reprojection converts a GeoDataFrame's coordinates from one CRS to another, recalculating every coordinate value so it still means the same real-world location under the new system. Unlike set_crs() (which only relabels and changes no numbers), to_crs() actually transforms the numbers.
IN PRACTICE
gdf_utm = gdf.to_crs('EPSG:32618')
Every coordinate is recalculated from degrees of longitude/latitude into meters of UTM easting/northing. The location on the ground does not move -- only the numbers describing it change, and a NEW GeoDataFrame is returned.
COMMON CONFUSION
Calling to_crs() on a GeoDataFrame whose crs is None raises a ValueError: 'Cannot transform naive geometries. Please set a crs on the object first.' Set the CRS before you reproject.
Notes: Timing: 2 minutes.
Teaching notes: Contrast directly with the previous slide's set_crs - set_crs labels, to_crs transforms. This is the single most common Week 7 mix-up.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/projections.html
[/Sources]

## Slide 16
ANATOMY
Explode one reprojection call into its parts
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
16
gdf_utm = gdf.to_crs('EPSG:32618')
1
1
New GeoDataFrame
to_crs() returns a NEW object -- it never modifies gdf in place.
2
2
Original GeoDataFrame
Still holds its current CRS and coordinates, untouched.
3
3
Reprojection
Recalculates every coordinate into the target CRS.
4
4
Target CRS
UTM zone 18N, meters -- the correct choice for Syracuse, NY.
Notes: Timing: 2 minutes.
Teaching notes: Walk left to right: a new name is created, the old GeoDataFrame is read but not changed, the method does the recalculation, and the string argument names the destination CRS.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/projections.html
[/Sources]

## Slide 17
PRINCIPLE
Degrees of latitude/longitude are not a ruler
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
17
A geographic CRS (like EPSG:4326) stores angles on a sphere. A projected CRS (like EPSG:32618) stores flat, linear meters.
Area and length calculations need a consistent linear unit. Only a projected CRS gives you one - so reproject before you measure.
Notes: Timing: 2 minutes.
Teaching notes: This is the single most important idea in today's deck. Everything after this slide is proof.

## Slide 18
VISUAL EVIDENCE
The same two zones, measured twice
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
18
Identical geometry, two coordinate systems. Only the right-hand number is an area.
Neither call raised an error
Both panels ran .area on the same polygons. The left returned 2.65e-08 - real arithmetic in square degrees, a unit that does not describe ground area. The right returned 239.74 m2 against a known 240. The danger is that the wrong answer looks like an answer; nothing crashed.
Notes: Timing: 2 minutes.
Teaching notes: Ask what a student would conclude if they only ever saw the left panel's number and did not know what unit it was in. That is the whole case for stating your EPSG code.

## Slide 19
PYTHON SYNTAX
DEMO 1 - measure 8.0 m apart directly in EPSG:4326
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
19
import geopandas as gpd
from shapely.geometry import Point
# R101, R102 are 8.0 m apart on the ground
p1 = Point(-76.1350754186006, 43.03940661157025)
p2 = Point(-76.134977093003, 43.03940661157025)
gdf = gpd.GeoDataFrame({'room_id': ['R101', 'R102']}, geometry=[p1, p2], crs='EPSG:4326')
d_geo = gdf.geometry.iloc[0].distance(gdf.geometry.iloc[1])
print(f'distance in EPSG:4326 (degrees): {d_geo:.6f}')
OUTPUT
distance in EPSG:4326 (degrees): 0.000098
0.000098 what?
Two Radley Hall rooms known to be 8.0 m apart on the ground. Measured directly in EPSG:4326 (still degrees of longitude/latitude), .distance() returns 0.000098 -- a number of DEGREES, meaningless as a physical distance. The next slide reprojects and measures again.
Notes: Timing: 2 minutes.
Teaching notes: This is the shared, pre-verified Radley Hall CRS demonstration from data/README.md - use these exact numbers, do not recompute different ones. Let students sit with 0.000098 for a moment before revealing what it actually represents.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/projections.html
[/Sources]

## Slide 20
PYTHON SYNTAX
DEMO 1, continued - reproject, then measure again
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
20
# gdf is still in EPSG:4326, from the previous slide
gdf_utm = gdf.to_crs('EPSG:32618')
d_utm = gdf_utm.geometry.iloc[0].distance(
gdf_utm.geometry.iloc[1]
)
print(f'distance in EPSG:32618 (meters): {d_utm:.3f}')
OUTPUT
distance in EPSG:32618 (meters): 8.010
8.010 m -- within 1 cm of the truth
to_crs('EPSG:32618') reprojects gdf to UTM zone 18N (meters, the correct choice for Syracuse, NY); the same two points now measure 8.010 m -- within 0.010 m of the known 8.000 m ground truth. The small remainder is real projection distortion, not a mistake.
Notes: Timing: 2 minutes.
Teaching notes: Reveal this only after students have sat with how meaningless 0.000098 degrees is. Tie 8.010 m explicitly back to the known 8.000 m ground truth - the small gap is real distortion, not an error.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/projections.html
[/Sources]

## Slide 21
PREDICT BEFORE YOU RUN
Predict: what happens when you call .area in EPSG:4326?
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
21
import geopandas as gpd
zones = gpd.read_file('zone_footprints.geojson')
print(zones.crs)
areas = zones.geometry.area
print(areas)
zones is still in EPSG:4326 (degrees). What happens next?
A
Raises an error and stops
B
Warns, but still returns a number
C
Reprojects automatically first
D
Returns NaN for every zone
ANSWER · B
GeoPandas warns but still returns a number -- a tiny, meaningless square-degree value. It never reprojects for you automatically.
Notes: Timing: 2 minutes.
Teaching notes: Take a show of hands on every option before revealing. Many predict an error, since a value this wrong feels like it should stop the script - it does not.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/projections.html
[/Sources]

## Slide 22
PYTHON SYNTAX
DEMO 2 - the same 240 m2 zone, measured two ways
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
22
import geopandas as gpd
zones = gpd.read_file('zone_footprints.geojson')
for zone, a in zip(zones['zone'], zones.geometry.area):
print(f'{zone}: {a:.2e} sq deg')
zones_utm = zones.to_crs('EPSG:32618')
for zone, a in zip(zones_utm['zone'], zones_utm.geometry.area):
print(f'{zone}: {a:.2f} m2')
OUTPUT
North: 2.65e-08 sq deg
South: 2.65e-08 sq deg
North: 239.74 m2
South: 239.74 m2
GeoPandas even warns you
Calling .area directly on EPSG:4326 geometry actually raises a UserWarning: 'Geometry is in a geographic CRS. Results from 'area' are likely incorrect.' (real, but printed to the console, not to the output panel here). Each Radley Hall zone is a 24 m x 10 m rectangle - 240 m2 by construction. Reprojected to EPSG:32618, both zones measure 239.74 m2: within about 0.1% of the known ground truth - a small, honest projection distortion, not an error.
Notes: Timing: 3 minutes.
Teaching notes: Read the real geopandas UserWarning text aloud once, unsuppressed, so students recognize it in their own console later. Tie 239.74 m2 forward explicitly - this is the exact number Meeting B's studio will reproduce.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/projections.html
[/Sources]

## Slide 23
READ THE DATA
Same pattern, both times: reproject before you measure
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
23
quantity
measured in EPSG:4326
measured in EPSG:32618
known ground truth
distance (R101-R102)
0.000098 (degrees)
8.010 m
8.000 m
zone footprint area
2.65e-08 (square degrees)
239.74 m2
240.00 m2
ARCHITECTURAL LENS
Geographic-CRS numbers are not wrong arithmetic - they are the right math applied to the wrong unit.
Notes: Timing: 2 minutes.
Teaching notes: Have students say out loud, for each row, which column they would actually trust and why. The projected-CRS column is always within a fraction of a percent of ground truth; the geographic-CRS column is off by many orders of magnitude.

## Slide 24
METHOD
Store globally, reproject locally, then measure
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
24
01
EPSG:4326
Store location
Longitude and latitude describe angular position in degrees.
02
SITE
Choose projection
Select a projected CRS whose valid zone contains the site.
03
EPSG:32618
Work in meters
UTM 18N supplies linear units appropriate for the Syracuse example.
04
MEASURE
Check distance/area
Compute only after reprojection and compare with a known scale.
Notes: Timing: 2 minutes.
Teaching notes: State the choice rule plainly: use a projection whose valid area contains the site. The fourth node keeps verification attached to the conversion.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/projections.html
[/Sources]

## Slide 25
IN-CLASS CHECK
Predict, then verify: which number would you trust?
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
25
Given a distance printed as 0.000041 in one CRS and 3.9 m in another, which is usable?
WORK THROUGH IT
1.
Identify which CRS is geographic and which is projected.
2.
State your prediction and why, before running anything.
3.
Reproject the geographic version to EPSG:32618 and compare.
4.
Write one sentence naming the correct CRS for a Syracuse, NY site.
Notes: Timing: 4 minutes.
Teaching notes: Expected answer: the projected (meters) value is usable; the geographic value is degrees, not a distance. Reinforces DEMO 1 with a fresh, unseen number.

## Slide 26
VOCABULARY
Buffer, defined
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
26
TERM
.buffer(distance)
.buffer(distance) returns a new polygon: every point within distance of the original geometry. Call it on a point to get a disc-shaped review radius; on a line to get a corridor; on a polygon to get a setback or expansion.
IN PRACTICE
site_marker.buffer(5.0)
On a GeoDataFrame already in EPSG:32618 (meters), buffer(5.0) returns a circular review zone with radius 5 m -- area near pi * 5^2 = 78.54 m2, verified on the next slide.
COMMON CONFUSION
distance is read in the GeoDataFrame's CURRENT CRS units. Buffer a point still in EPSG:4326 and distance means degrees, not meters -- reproject first, exactly like DEMO 1 and DEMO 2.
Notes: Timing: 3 minutes.
Teaching notes: Connect directly back to the two demos: buffer is just another operation that silently uses the wrong unit if you skip reprojecting.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/projections.html
[/Sources]

## Slide 27
PYTHON SYNTAX
A 5 m buffer should have about pi times 5 squared area
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
27
import math
import geopandas as gpd
from shapely.geometry import Point
site_marker = gpd.GeoDataFrame({'id': [1]}, geometry=[Point(0.0, 0.0)], crs='EPSG:32618')
review_zone = site_marker.buffer(5.0)
print(review_zone.geom_type.iloc[0])
print(f'area: {review_zone.area.iloc[0]:.2f} m2')
print(f'pi * r^2 check: {math.pi * 5.0**2:.2f} m2')
OUTPUT
Polygon
area: 78.41 m2
pi * r^2 check: 78.54 m2
A circle is really a many-sided polygon
buffer() returns a Polygon - internally, a many-sided approximation of a circle. Its area, 78.41 m2, sits just under the true circle area of 78.54 m2 (pi x 5^2) because the polygon approximation has a finite number of straight sides. This is a real, honest approximation, not a bug.
Notes: Timing: 3 minutes.
Teaching notes: Ask what would happen to that 78.41 vs 78.54 gap with a coarser or finer buffer resolution - not required to demo, just to build intuition that buffer is an approximation.
[Sources]
- https://geopandas.org/en/stable/getting_started/introduction.html
[/Sources]

## Slide 28
VOCABULARY
Spatial join, defined
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
28
TERM
gpd.sjoin()
A spatial join matches rows between two GeoDataFrames by their spatial relationship -- for example, which point falls within which polygon -- instead of by a shared column value like an ordinary merge.
IN PRACTICE
gpd.sjoin(markers, zones, how='left', predicate='within')
Attaches each zone's attributes to every marker point that falls within it. Both inputs must share the same CRS first, exactly as an ordinary merge needs a shared key column.
COMMON CONFUSION
how='left' keeps every row from markers, even a point inside no polygon (its new column becomes NaN). how='inner', the default if you omit how, would silently drop that row instead.
Notes: Timing: 2 minutes.
Teaching notes: Draw the parallel to Week 5 merge: a table merge matches values; a spatial join matches geometry. Both inputs must share a CRS.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/mapping.html
[/Sources]

## Slide 29
METHOD
A spatial join uses location as the key
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
29
01
LEFT
Points
Each marker keeps its identity and geometry.
02
RIGHT
Polygons
Each zone carries attributes such as name or category.
03
PREDICATE
Test relation
within, intersects, or contains defines what counts as a match.
04
RESULT
Attach attributes
Matched zone information is added to each point row; unmatched rows remain visible.
Notes: Timing: 3 minutes.
Teaching notes: Walk through the four boxes using the upcoming three-point/two-polygon example before students see any code - LEFT is markers, RIGHT is zones, PREDICATE picks the rule, RESULT attaches attributes.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/mapping.html
[/Sources]

## Slide 30
PYTHON SYNTAX
Three site markers, two zone polygons: set up both layers
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
30
import geopandas as gpd
from shapely.geometry import Point, Polygon
markers = gpd.GeoDataFrame({'site_id': ['S1','S2','S3']}, geometry=[Point(5,5), Point(5,15), Point(30,30)], crs='EPSG:32618')
zone_a = Polygon([(0,0), (10,0), (10,10), (0,10)])
zone_b = Polygon([(0,10), (10,10), (10,20), (0,20)])
zones = gpd.GeoDataFrame({'zone_name': ['Zone A', 'Zone B']}, geometry=[zone_a, zone_b], crs='EPSG:32618')
print(markers.crs == zones.crs)
OUTPUT
True
Same CRS, required before any join
S1 and S2 sit inside the two zone polygons; S3 sits well outside both. Both GeoDataFrames are built directly in EPSG:32618 (meters), so the join on the next slide can safely test within/intersects using real distances, not degrees. Confirming markers.crs == zones.crs is a habit worth keeping before every spatial join.
Notes: Timing: 2 minutes.
Teaching notes: Trace the three points and two boxes on the board now, before the predict slide asks students to reason about S3 -- this is the setup they need in hand.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/mapping.html
[/Sources]

## Slide 31
PREDICT BEFORE YOU RUN
Predict: what happens to the point outside every zone?
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
31
joined = gpd.sjoin(
markers, zones,
how='left', predicate='within',
)
print(len(joined))
S3 falls outside both zone polygons. What does len(joined) print?
A
3 -- kept, S3's zone is NaN
B
2 -- S3 dropped, no match
C
Raises a ValueError
D
0 -- needs a shared column first
ANSWER · A
how='left' keeps every row, even S3. how='inner' (the default) would drop it and print 2. A join matches by location, not a shared column.
Notes: Timing: 2 minutes.
Teaching notes: Most predict 2, remembering merge's default inner-join behavior and not tracking the how='left' argument. Reveal, then run the real code on the next slide.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/mapping.html
[/Sources]

## Slide 32
PYTHON SYNTAX
Run the spatial join: who is where?
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
32
joined = gpd.sjoin(markers, zones, how='left', predicate='within')
print(joined[['site_id', 'zone_name']])
OUTPUT
site_id zone_name
0 S1 Zone A
1 S2 Zone B
2 S3 NaN
NaN is honest, useful information
S1 falls inside Zone A, S2 inside Zone B. S3 sits outside both polygons entirely, so how='left' keeps it in the result with zone_name as NaN - the point exists, it just is not inside any known zone. That NaN is real information, not a failure.
Notes: Timing: 2 minutes.
Teaching notes: Trace all three points against the two boxes on the board before revealing the printed table - this is exactly the kind of prediction step Meeting B's studio will ask for.
[Sources]
- https://geopandas.org/en/stable/docs/user_guide/mapping.html
[/Sources]

## Slide 33
A DESIGN DECISION, EXPLAINED
Why this course does not spatial-join individual rooms
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
33
The pitfall
Radley Hall's room coordinates repeat: the same x_m, y_m location holds a room on floor 1, floor 2, and floor 3 (a real multi-story footprint). A point-in-polygon join on individual rooms would match several stacked rooms to the same zone at once - confusing, not wrong.
The fix Meeting B uses instead
Summarize first (Week 5's groupby, by zone), THEN join that one summary row per zone onto the zone polygon. One row per zone avoids the stacked-floor ambiguity completely, and is exactly the workflow needed if you choose the map for Project 1 Part IV -- one of two evidence-extension choices, alongside Week 6's animation.
Notes: Timing: 3 minutes.
Teaching notes: Be explicit that this is a modeling choice driven by the data's real structure, not a limitation of spatial joins in general - the toy S1/S2/S3 example above is exactly where a row-level join DOES make sense (one row, one place).

## Slide 34
IN-CLASS CHECK
Transfer the spatial join: which entrances fall inside shaded zones?
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
34
Entrance points and shade polygons arrive in EPSG:4326; the team also needs a 5 m review radius around each entrance.
WORK THROUGH IT
1.
Choose the point and polygon geometry roles and inspect both CRS values.
2.
Reproject to EPSG:32618 before buffering or measuring distance.
3.
Predict within versus intersects for an entrance exactly on a shade boundary.
4.
Verify matched and unmatched points, then state the boundary rule used.
Notes: Timing: 4 minutes.
Teaching notes: The point-in-polygon join can be evaluated in a shared CRS, but any 5 m buffer or distance requires the projected CRS. A boundary point may fail within yet satisfy intersects; the team must state which predicate matches the decision. Require a visual or row-level check of unmatched entrances rather than trusting only the join count.

## Slide 35
METHOD
The correct spatial workflow, every time
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
35
01
LOAD
Read the geometry
gpd.read_file() and note its CRS immediately - do not assume.
02
CHECK
Confirm the CRS
Geographic (degrees) or projected (meters)? Read the EPSG code.
03
REPROJECT
to_crs() before measuring
Convert to a projected CRS (EPSG:32618 for Syracuse, NY) before any area, length, buffer, or distance.
04
COMPUTE
Measure or join
Now .area, .length, .buffer(), and sjoin() all return trustworthy, checkable numbers.
Notes: Timing: 2 minutes.
Teaching notes: This four-step order is the single procedural takeaway students should be able to recite before Wednesday's studio.

## Slide 36
2026 PRACTICE HORIZON
Spatial evidence now moves through open files and web APIs
ARC 500 · Week 7 · Meeting A · Spatial Data, Scale, and Maps
36
01
PACKAGE
GeoParquet
Geometry columns travel with declared encoding and CRS metadata in a columnar file.
02
DISCOVER
OGC API collections
A client can discover available feature collections, extents, and capabilities.
03
QUERY
Request a bounded subset
Filter by collection, spatial or attribute criteria, and only the fields needed.
04
VERIFY
Inspect before measuring
Check schema, CRS, axis order, extent, missing geometry, and unmatched features.
Notes: Timing: 2 minutes.
Teaching notes: Optional horizon slide. GeoParquet and OGC APIs change delivery, not geometric truth. Rehearse the same refusal: do not measure distance or area until CRS and geometry validity are understood.
[Sources]
- https://geoparquet.org/releases/v1.1.0/
- https://ogcapi.ogc.org/features/overview.html
[/Sources]

## Slide 37
WEEK 7 · MEETING A · SPATIAL DATA, SCALE, AND MAPS
Geometry plus a trustworthy CRS is what makes a map true
01
Geometry (where) and attributes (what) are separate; a GeoDataFrame just adds a geometry column and a CRS to pandas.
02
EPSG:4326 (degrees) is for storage and sharing; EPSG:32618 (meters, UTM 18N) is for measuring at Syracuse, NY.
03
Reproject to a projected CRS before computing area, length, buffer, or distance - geographic-CRS numbers are real math applied to the wrong unit.
04
buffer() and sjoin() extend this same CRS discipline to proximity and location-based joins.
Notes: Timing: 1 minutes.
Teaching notes: Exit ticket: students write the EPSG code they will use for their own Project 1 site and one sentence justifying it.